## Slide 1: NVIDIA Jetson Nano: Specs & Model deployment
ZHI Xiaoying & WANG Xuan

## Slide 2: Why we dropped Google Coral
Success: Train ResNet with Quantization-aware training
Failure: Continue to train DeepLabCut with Quantization-aware training
Failure from: datatype mismatch in TensorFlow library
Mismatch waiting to be fixed
Still another approach: rewrite the DLC model, so that it does not load ResNet and continue training, but train from the very start as a whole

## Slide 3: Hardware Components
Storage: micro-SD card
Power: micro-USB / power jack
Ethernet port
HDMI / DisplayPort
MIPI CSI camera
E.g. Raspberry Pi camera module V2

## Slide 4: SDK: NVIDIA JetPack
OS: Full desktop Linux with NVIDIA driver
AI & CV libraries and APIs
  TensorRT, cuDNN, CUDA
  VisionWorks & CV
  Camera application API
  Sensor driver API
Developer tools
  Nsight Systems
  Nsight Graphics
New version features:
Docker enabled
TensorRT support for INT-8 DLA operations
Notes: Nsight Systems is a system-wide performance analysis tool for visualization of application’s algorithms.
Nsight Graphics is a developer tool for debugging, profiling and exporting frames.
DLA: deep learning accelerator

## Slide 5: Jetson Nano vs. Google Coral
Jetson Nano
Price: $99
Size: 69.6mm x 45mm
Linux distri: Ubuntu 18.04
AI Accelerator: 128 CUDA cores
RAM: 4GB
Flash: 16GB
Performance: faster in some cases, slower in others
Google Coral
Price: $149
Size: 88mm x 22mm
Linux distri: Mendel (32-bit)
AI Accelerator: Edge TPU
RAM: 1GB LPDDR4
Flash: 8GB
https://towardsdatascience.com/google-coral-edge-tpu-board-vs-nvidia-jetson-nano-dev-board-hardware-comparison-31660a8bda88
Notes: BLE: bluetooth low energy

## Slide 7
https://www.jianshu.com/p/dd2cfc33b437
Install Corresponding TF API;
Configure as required
Download and build from checkpoint
Create TensorRT inference graph;
Save in required format
Load the TensorRT graph
Run and make a prediction